# Airspeed Limitations:

| Speed Name/Remarks | Indicated Airspeed |
| --- | --- |
|  | Knots | MPH |
| VNE | Never Exceed Speed Do not exceed this speed in any operation | 160 | 184 |
| VNO | Max structural cruising speed Do not exceed this speed except in smooth air and then only with caution | 128 | 147 |
| VA | Maneuvering speed 2300 Pounds 1950 Pounds 1600 Pounds | 97 89 80 | 111 102 92 |
| VFE | Maximum flap extended speed | 85 | 97 |
|  | Maximum window open speed | 158 | 184 |
| VS | Stall speed (No Flaps) | 47 | 54 |
| VS0 | Stall speed in landing configuration | 41 | 47 |
|  | Demonstrated Crosswind capability | 15 | 17 |

# Maneuvering Limits

| Speed Name/Remarks | Max Indicated Airspeed |
| --- | --- |
|  | Knots | MPH |
| Chandelles | 105 | 120 |
| Lazy Eights | 105 | 120 |
| Steep Turns | 95 | 109 |
| Spins | Use slow deceleration |
| Stalls (except whip stalls) | Use slow deceleration |

Stall Speed Table (Max Gross/CG Forward):

| Angle of Bank | 00 Flaps | 400 Flaps |
| --- | --- | --- |
|  | KIAS | MPH | KIAS | MPH |
| 00 | 47 | 54 | 41 | 47 |
| 300 | 51 | 59 | 44 | 51 |
| 450 | 56 | 64 | 49 | 56 |
| 600 | 66 | 76 | 58 | 67 |

# Optimum/Recommended Speeds:

| Speed Name/Remarks | Indicated Airspeed |
| --- | --- |
|  | Knots | MPH |
| VX | Best angle of climb | 59 | 68 |
| VY | Best rate of climb | 73 | 84 |
| VR | Normal rotation | 55 | 63 |
|  | Normal climb | 70 - 80 | 80 - 92 |
|  | Normal landing (no flaps) | 60 - 70 | 69 - 80 |
|  | Normal landing (full flaps) | 55 - 65 | 63 - 75 |
|  | Powered landing (no flaps) | 65 | 75 |
|  | Powered landing (full flaps) | 60 | 69 |
|  | Max performance approach | 60 | 69 |
|  | Optimum glide | 65 | 75 |

# Engine Failure During Takeoff Run:

Throttle	Idle

Brakes	Apply

Flaps	Retract

Mixture	Idle Cutoff

Ignition Switch	Off

Master Switch	Off

# Engine Failure Immediately After Takeoff

1.	If enough runway remaining to land:

Throttle	Idle

Land airplane

Brakes	Apply

Flaps	Up

Mixture	Idle cutoff

Ignition Switch	Off

Master Switch	Off

- Not enough runway to land

Airspeed	60 KIAS (69 MPH)

Fly runway heading to emergency landing site

Mixture	Idle cutoff

Fuel Selector	Off

Ignition switch	Off

Flaps	As required

Master switch	Off

Doors	Ajar

# Engine Failure In Flight:

1.	Gain all the altitude you can!

Pull back (gently) to use the aircraft’s momentum to gain altitude until airspeed falls off to the optimum glide speed (65 KIAS - 75 MPH).

2.	Airspeed - Optimum glide speed 65 KIAS (75 MPH)

Trim the airplane for optimum glide speed..

3.	Find a suitable place to land and fly to it

If altitude and distance to selected site permit, try to set up a normal landing pattern. If that’s not possible, take what you can get. Regardless of whether or not a full pattern can be set up, make sure the approach results in a landing parallel to any furrows in the selected field.

4.	If time permits, try to correct the problem

Fuel Selector	Both

Mixture	Rich (in)

Throttle	1/4 Inch

Carburetor Heat	On (out)

Primer	In and Locked

Master Switch	On (Both sides)

Ignition switch	Both magnetos
Start - if propeller is stopped.

5.	If still have time communicate

Transponder	7700

Comm Radio	121.5

# Emergency Landing Without Engine Power:

1.	Fly the airplane

AIrspeed	65 KIAS / 75 MPH (flaps up)
60 KIAS / 69 MPH (flaps down)

2.	Prepare aircraft for landing

Mixture	Idle cutoff

Fuel Selector	Off

Ignition Switch	Off

Flaps	As required (40o recommended)

Master Switch	Off

Doors	Unlatch prior to touchdown

3.	Landing

Touchdown	Slightly tail low

Brakes	Apply heavily

# Precautionary Landing With Engine Power

1.	Fly the airplane

Airspeed	60 KIAS (69 MPH)

Flaps	20o

Selected Field	Inspect

Fly over field noting terrain and obstructions then retract flaps upon reaching a safe altitude and airspeed.

2.	Prepare airplane for landing

Radios and Electrical	Off

Flaps	30o (On final approach)

Airspeed	55 KIAS (64 MPH) on final

Master Switch	Off

Doors	Unlatch prior to touchdown

3.	Landing

Touchdown	Tail slightly low

Ignition Switch	Off

Brakes	Apply heavily

# Ditching:

1.	Prepare for ditching

Radio	Transmit MAYDAY on 121.5

Give location, situation and intentions.

Note, if you were already communicating with ATC, report situation to controller, as opposed to using 121.5.

Transponder	7700

Heavy Baggage	Secure or jettison

2.	Fly the airplane

Approach

High wind / Heavy seas - Into the wind

Light winds / Heavy swells - Parallel to the swells

Flaps	20o - 40o

Power	300 ft./min. descent, 55 KIAS (64 MPH).

Cabin Doors	Unlatch prior to touchdown

3.	Landing

Touchdown	Level attitude at 300 ft./min. descent

Face	Cushion with folded coat

Evacuate	Through doors.

If necessary, open windows to allow cabin to flood to equalize pressure so doors can be opened.

Life Vests and Raft	Inflate

# Engine Fire During Start Up:

Cranking	Continue

Getting the engine to start will suck flames and accumulated fuel into the engine.

If Engine Starts

Power - 1,700 RPM for a few minutes

Engine - Shutdown and inspect for damage.

If Engine Fails to Start

Throttle - Full Open

Mixture - Idle Cutoff

Continue cranking for 2 to 3 minutes.

Obtain fire extinguisher

Master Switch - Off

Ignition Switch - Off

Fuel Selector - Off

Extinguish fire with extinguisher, seat cushion, blanket, etc. or dirt.

Inspect for damage and have repairs made before attempting another flight.

# Engine Fire In Flight:

Mixture	Idle cutoff

Fuel Selector	Off

Master Switch	Off

Cabin Heat and Air	Off (except overhead vents)

Airspeed	100 KIAS (115 MPH)

If that does not extinguish the fire increase airspeed to that which produces an incombustible mixture.

Be aware of critical speeds; VNO (128 KIAS/147 MPH) and VNE (158 KIAS/181 MPH).

Landing	Forced Landing Without Power

# Electrical Fire In Flight:

1.	Extinguish Fire

Master Switch	Off

All other Switches	Off

Ignition	On

Vents, Cabin Heat/Air	Closed

Fire Extinguisher	Activate

2.	If fire appears to be out and electrical equipment is needed

Master Switch	On

Circuit Breakers	Check for faulty circuit - do not reset.

Radio/Electrical	On one at a time, with delay between until short circuit is localized.

Vents, Cabin Heat/Air	Open once it is ascertained that the fire is completely extinguished.

# Cabin Fire:

Master Switch	Off

Vents, Cabin Heat/Air	Closed

Fire Extinguisher	Activate

After using fire extinguisher within a closed cabin ventilate the cabin.

Landing	As soon as possible

# Wing Fire

Navigation lights	Off

Strobe Lights	Off

Pitot Heat	Off

Attitude

Perform side-slip to keep the flames away from the fuel tank and cabin.

Land	ASAP

Do not use flaps.

# Pre-Flight Inspection Checklist:

1.	Wing Tops/Fuel Tanks

Fuel Level	Both Wings - Visual check

If needed get gas (AVGAS 100) before proceeding with other fuel tank related items.

Filler caps	Both Wings - Secure

Make sure vent on right wing cap is not blocked.

Wing Tops	Inspect for loose screws, rivets and damage

2.	Cockpit

Control wheel lock	Remove

Ignition switch	Off

Master switch	On (both sides)

Fuel gauges	Check quantity

Flaps	10o

Pitot Heat	On - observe Ammeter drop - then off

Strobe/Beacon	On - visually check - off

Master Switch	Off

Fuel shut-off valve	On

Paperwork:

Airworthiness certificate

Registration

Radio station license

Operating limitations (POH)

Weight/loading data

3.	Cockpit - Night Flights

Nav Lights & Strobes	On

Walk around plane and visually check to see that all are operating.

Landing Light	On

Visually check from outside if not dark enough to see that it’s on from inside the cockpit.

Instrument Lights	On

4.	Fuselage - Left Side

Baggage Door	Locked with key

Radio antennas	Check security

Miscellaneous	Check for loose screws/rivets, etc.

5.	Empennage

Rudder gust lock	Remove

Tail tie-down	Disconnect

Control surfaces	Check freedom of movement, actuators, security, loose rivets, damage.

6.	Fuselage Right Side

Miscellaneous	Check for loose screws/rivets, etc.

Fuel strainer drain (belly)	Check sample for water/dirt
(some models)

7.	Right Wing

Flaps	Check actuator and rollers

Aileron	Check freedom, hinge pins and counterweights

Wing tip	Check for cracks
Check navigation light

Leading edge	Check for dents, cracks, etc.

Wing tie-down	Disconnect

Main wheel tire	Check for proper inflation/wear
Check cotter pin in wheel nut

Main wheel brake	Check for fluid leaks
Check brake pads

Fuel drain	Check sample for water/dirt and fuel type (100LL - Blue)

8.	Nose

Engine Oil	Check level

Note: Different versions of C-172 have different oil capacities

Fuel bowl drain	Check sample for water/dirt and fuel type (100LL - Blue)

Prop/Spinner	Check for nicks and security

Air filter	Check for restrictions & excessive dirt

Landing Light	Check condition and cleanliness

Cowling	Look for birds or nests inside

Nose wheel	Check for proper inflation/wear; Check for cotter pins in wheel nuts;
Check for leaking fluids

Nose tie-down	Disconnect

Static source opening	Check not blocked

9.	Left Wing

Wing tie-down	Disconnect

Leading edge	Check for dents, cracks, etc.

Pitot tube	Remove cover check for blockage

Stall warning opening	Check for blockage

Fuel Tank Vent	Check for blockage

Wing tip	Check for cracks
Check navigation light

Aileron	Check freedom, hinge pins and counterweights

Flaps	Check actuator and rollers

Fuel drain	Check sample for water/dirt and fuel type (100LL - Blue)

Main wheel tire	Check for proper inflation/wear
Check cotter pin in wheel nut

Main wheel brake	Check for fluid leaks
Check brake pads

# Normal Engine Starting Checklist:

1.	Before Starting

Preflight Inspection	Completed

Seat position	Adjust & ensure locked

Seal belts/harness	Adjust and lock

Brief passengers on use of belts/harnesses and requirements for wearing them.

Fuel Selector	Both

Radios/electrical	Off

Autopilot	Off

Brakes	Test and set

Circuit Breakers	Check all in

2.	Starting Engine

Mixture	Rich (in)

Carburetor heat	Cold (in)

Primer	Prime if required
Make sure locked in

Throttle	1/8 Inch

Key	In ignition

Master Switch	On (both sides)

Propeller Area	Call “Clear” & check prop area and behind plane

Ignition	Start - release on start

Throttle	1,000 RPM

Oil Pressure	Check in green

3.	Before Taxiing

Radios	On and set to appropriate frequency. Call for radio check

Transponder	Standby

Beacon/Strobe	On

Nav. Lights/Strobes	On if required

Flaps	Full up (normal takeoff)

4.	Taxiing

Clearance	Check for things in way of wings
Check for people ahead of and behind plane

Flight Controls	Set for existing wind conditions

Brakes	Come to full stop immediately after starting taxi roll

- IFR Instrument Checks

Turn Coordinator	Should indicate turn in proper direction while taxiing.

Attitude Indicator	Very little change due to turns; Slight pitch indications due to acceleration or deceleration.

Heading Indicator	Should track headings.

Altimeter	When set to current altimeter setting should indicate within 75 ft. of airport elevation.

VSI	Should indicate zero. If not, note indication and use for level indication in flight.

VORs	Check at local ground check point or against each other based on some receivable signal.

# Cold Weather Starting Without Pre-Heat:

1.	Before Starting

Preflight Inspection	Completed

Seat position	Adjust & ensure locked

Seal belts/harness	Adjust and lock

Brief passengers on use of belts/harnesses and requirements for wearing them.

Fuel Selector	Both

Radios/electrical	Off

Autopilot	Off

Brakes	Test and set

Circuit Breakers	Check all in

2.	Starting Engine

Ignition	Off (take key out and hang it up)

Master Switch	Off (both sides)

Prime

With ignition switch off and throttle closed, prime the engine four to ten strokes as the propeller is being turned by hand. Use heavy primer strokes for best atomization of fuel.

If doing this by yourself, tie the plane down securely and set parking brake, in case engine starts.

Treat propeller as if the ignition is on and engine could start.

Leave primer charged and ready for a stroke.

Propeller Area	Clear

Master Switch	On

Mixture	Full Rich

Throttle	Open 1/8 inch

Ignition Switch	Start

Throttle	Pump to full open twice then return to 1/8 inch open position.

Primer	Continue to prime until engine is running smoothly. Alternately pump throttle rapidly over first 1/4 of travel.

Oil Pressure	In the green

This might take a little time since the engine is cold. If pressure doesn’t come up in about 30 seconds, shut the engine down.

Carburetor Heat	Full on after engine started. Leave on until running smoothly.

Primer	In and locked.

Caution:

If engine does not start during the first few attempts, or if engine firing diminishes in strength, it is probable that the spark plugs have frosted over. Pre-heat must be used before another start is attempted.

Caution:

Pumping the throttle may cause raw fuel to accumulate in the intake air duct, creating a fire hazard in the event of a back-fire. If this occurs, maintain a cranking action to suck flames into the engine. An outside attendant with a fire extinguisher is advised for cold starts without pre-heat.

3.	Perform steps 3 through 5 on normal start checklist

# Cold Weather Starting With Pre-Heat:

1.	Before Starting

Preflight Inspection	Completed

Seat position	Adjust & ensure locked

Seal belts/harness	Adjust and lock

Brief passengers on use of belts/harnesses and requirements for wearing them.

Fuel Selector	Both

Radios/electrical	Off

Autopilot	Off

Brakes	Test and set

Circuit Breakers	Check all in

2.	Starting Engine

Ignition	Off (take key out and hang it up)

Master Switch	Off (both sides)

Prime

With ignition switch off and throttle closed, prime the engine two to four strokes (up to seven without pre-heat) as the propeller is being turned by hand. Use heavy primer strokes for best atomization of fuel.

If doing this by yourself, tie the plane down securely and set parking brake, in case engine starts.

Treat propeller as if the ignition is on and engine could start.

Primer	In and locked

Propeller Area	Clear

Master Switch	On

Mixture	Full Rich

Throttle	Open 1/8 inch

Ignition Switch	Start

Throttle	1,000 RPM.

Oil Pressure	In the green

This might take a little time since the engine is cold. If pressure doesn’t come up in about 30 seconds, shut the engine down.

3.	Perform steps 3 through 5 on normal start checklist

# Before Takeoff Checklist:

1.	Final Cockpit Check

Cabin doors	Closed and latched

Windows	Closed

Flight Controls	Free and correct

Elevator trim	Takeoff position

Rudder trim	Takeoff position

Flight Instruments	Check and set

Set attitude indicator to level flight position

Set altimeter to runway altitude or locally reported altimeter setting

Set heading indicator to magnetic compass

Comm Radio/VOR	Set to appropriate freqs

Beacon/Strobe	On

Nav Lights/Strobes	On if required

Autopilot	Off

2.	Engine Run-up

Fuel Selector	Both

Mixture	Rich (in)

Parking brake	Set or hold foot brakes

Throttle	1,700 RPM

Magnetos	Check

RPM drop should not exceed 125 RPM on either magneto.

RPM difference between magnetos should not exceed 50 RPM.

Carburetor Heat	On

Check for RPM drop then back to off

Engine instruments	Check

Oil pressure/Temperature

Ammeter - Create electrical load with landing light.
Make sure no more than needle width deflection.

Vacuum	Check in green

Throttle	Idle

Carburetor heat	On – Make sure engine keeps running

Throttle	1,000 RPM

Throttle friction lock	Adjust

Alternator switch	Off – Check low voltage light on – Switch back to on

Flaps	Appropriate takeoff position

Transponder	Set to mode C/Altitude

# Normal Takeoff and Climb Procedures

Flaps	Full up

Carburetor Heat	Cold (in)

Elevator Trim	Takeoff position

Rudder Trim	Takeoff position

Heading indicator	Calibrate against compass

Throttle	Full open (in)

Engine Instruments	Check while starting roll

RPM - 2600 (Top of green arc)

Oil Pressure - In the green

Oil Temperature - In the green

Suction - In the green

Airspeed	Building

Elevator	Lift nose wheel at 55 KIAS (63 MPH)

Climb Speed	70 - 80 KIAS (80 - 92 MPH)

# Maximum Performance Takeoff (Short Field):

Taxi	Maximum runway usage

Takeoff procedure should be started using ALL available runway. Taxi to end of runway and align with centerline.

Brakes	Set and hold

Flaps	Full up

Carburetor Heat	Cold (in)

Elevator Trim	Takeoff position

Rudder Trim	Takeoff position

Heading indicator	Calibrate against compass

Throttle	Full open (in)

Engine Instruments	Check before starting roll

RPM - 2600 (Top of green arc)

Oil Pressure - In the green

Oil Temperature - In the green

Suction - In the green

Brakes	Release

Airspeed	Building

Elevator	Slightly tail low

Climb Speed	59 KIAS (68 MPH) with obstacles ahead.

# Soft Field Takeoff:

Taxi	Keep rolling to avoid bogging down

Flaps	10o

If 10o flaps are used, with obstacles ahead, leave them extended until the obstacle is cleared and at a safe altitude.

The exception is in high density altitude takeoff where the climb would be marginal with the flaps at 10o.

Carburetor Heat	Cold (in)

Elevator Trim	Takeoff position

Rudder Trim	Takeoff position

Heading indicator	Calibrate against compass or runway heading

Throttle	Full open (in)

Engine Instruments	Check as starting roll

RPM - 2600 (Top of green arc)

Oil Pressure - In the green

Oil Temperature - In the green

Suction - In the green

Airspeed	Building

Elevator	Slightly tail low

Allow the airplane to lift off as soon as possible (before reaching safe climb speed). Level off at a few feet above the ground and fly in ground effect until reaching normal climb speed.

Climb Speed	55 KIAS (63 MPH) with obstacles ahead.

Flaps	Retract at safe altitude with positive rate of climb.

# After Takeoff Checklist

1.	Climbout

Airspeed	70 - 80 Knots (90 - 92 MPH)

Altitude	Above 300 AGL

Flaps	Up (in 10o increments if more than that in use)

2.	At Cruise Altitude

Attitude	Level

Airspeed	Let build to desired cruise speed

Throttle	Reduce to desired cruise setting

Heading Indicator	Calibrate against compass

3.	Above 3,000 MSL

Mixture	Lean for maximum RPM

# Enroute Climb:

Normal AIrspeed	70 - 85 KIAS (80 - 98 MPH)

Max Performance	See POH Climb Table in Section 5

Throttle	Full Open (in)

Carburetor Heat	Cold (in)

Mixture	Rich (in) below 3,000 ft.
Leaned for maximum RPM above 3,000.

# Normal Approach and Landing Procedures:

1.	Pre-Landing (Downwind) check

Seat belts/Harnesses	Adjust and lock

Mixture	Rich (In)

Carburetor heat	On (Out)

Fuel Selector	Both

Autopilot	Off

2.	Approach and Landing

Power	Reduce to 1,300 to 1,500 RPM abeam approach end of runway

Airspeed	Let bleed off to less than 85 KIAS (95 MPH)

Flaps	Use as desired

Under light (less than 10 Knots) wind conditions 10o descending on the end of the downwind leg, 20o on base, and full flaps over the threshold.

In heavier winds 20o or less is good flap setting for landing.

Use minimum flap setting possible for cross wind landing

Airspeeds

Downwind through base 65 - 75 KIAS (75 - 86 MPH)

Final approach 60 - 70 KIAS (70 - 80 MPH)

In gusty winds add 1/2 difference between gust and average wind speed to approach speed.

Touchdown

Just above stalling speed - main wheels first.

Landing Roll

Lower nose wheel gently

Braking

Minimum required.

# Short Field Landing:

1.	Pre-Landing (Downwind) check

Seat belts/Harnesses	Adjust and lock

Mixture	Rich (In)

Carburetor heat	On (Out)

Fuel Selector	Both

Autopilot	Off

2.	Approach and landing

Power	Reduce to 1,300 to 1,500 RPM abeam approach end of runway

Airspeed	Let bleed off to less than 85 KIAS (95 MPH)

Flaps

Under light (less than 10 Knots) wind conditions 10o descending on the end of the downwind leg, 20o on base, and full flaps on final.

Airspeeds

Downwind through base 65 - 75 KIAS (75 - 86 MPH)

Final approach 60 KIAS (69 MPH)

In gusty winds add 1/2 difference between gust and average wind speed to approach speed.

Touchdown

Just above stalling speed - power off - main wheels first.

Roundout must be done much faster than usual due to low airspeed.

Landing Roll	Lower nose wheel quickly.

Braking	Maximum possible without sliding tires.

Flight Controls	Raise flaps to decrease lift and improve braking.
Hold full nose up elevator

# Soft Field Landing:

1.	Pre-Landing (Downwind) check

Seat belts/Harnesses	Adjust and lock

Mixture	Rich (In)

Carburetor heat	On (Out)

Fuel Selector	Both

Autopilot	Off

2.	Approach and Landing

Power	Reduce to 1,300 to 1,500 RPM abeam approach end of runway

Airspeed	Let bleed off to less than 85 KIAS (95 MPH)

Flaps

Under light (less than 10 Knots) wind conditions 10o descending on the end of the downwind leg, 20o on base, and full flaps over the threshold.

In heavier winds 20o or less is good flap setting for landing.

Use minimum flap setting possible for cross wind landing

Airspeeds

Downwind through base 60 - 70 KIAS (69 - 80 MPH)

Final approach 55 - 65 KIAS (63 - 75 MPH)

In gusty winds add 1/2 difference between gust and average wind speed to approach speed.

Touchdown

Just above stalling speed - power off - main wheels first.

Landing Roll

Hold nose wheel off as long as possible.

Braking	As required

Flight Controls	Full up elevator

# Balked Landing (Go Around):

Throttle	Full Open (in)

Carburetor Heat	Cold (in)

Flaps	To 20o

If more than 20o of flaps were in when the go-around is initiated, retract immediately to 20o.

Continue to retract flaps in 10o increments only after establishing a positive rate of climb and reaching a safe altitude.

Airspeed	55 KIAS (63 MPH)

# Post-Landing Checklists:

1.	After Landing - Clear of Runway

Flaps	Full up (visual check)

Carburetor Heat	Off (in)

Elevator Trim	Takeoff position

Rudder Trim	Takeoff position

2.	If Hard Landing

ELT	Listen for on 121.5 on communications radio

3.	Engine Shutdown

Radios/Electrical	All off

Throttle	1,000 RPM

Mixture	Idle cutoff

Ignition	Off

Master Switch	Off

4.	Securing the Airplane

Parking Brake	Set

Control Lock	Install

Tiedown	Wings and Tail

Pitot Cover	Install

Double Check

All electrical equipment - Off

Master Switch - Off

- Close your Flight Plan

# Before Leaving Home

1.	Self Check

Feeling ok	Yes

Under any stress	No more than usual

Taking any medication	No

Alcohol in last 12 Hrs.	No

2.	Flight Planning/Navigation Equipment

Current Charts

A/FD

POH

Airport Guide

E6-B

Plotter

Calculator

Timer

Custom Checklists

Flight Plans

Weather Reports

Pencils

Clipboards

3.	Emergency Items

Hand Compass

Knife

Flashlights

Batteries

Bulbs

Cell Phone (Charged)

Spare Glasses

Sun Glasses